# Option to aggregate AvXML reports (bulletinization)

## Background

- AvXML is designed for the reporting of aviation operational meteorological information (OPMET).  In future, when AvXML reports are exchanged in net-centric environment, aggregation of reports will be taken care by the communication protocol (e.g. OGC Web Feature Service).

- At the moment, where OPMET reports are still being exchanged through store-and-forward message switching systems, an aggregation method is required to “bulletinize” the AvXML reports for downstream dissemination.

## Proposed application schema to aggregate AvXML reports

- Figure 1 shows the UML model of the proposed application schema to “bulletinize” AvXML reports.  It has the following features:

- Mimic existing GTS/AFTN bulletin structure with a header and payload

- The header contains gmd:MD_Metadata for the attachment of metadata

- Schematron rules are in place to enforce the requirement that only a single kind of reports are allowed in a bulletin

- A sample instance is attached in Appendix I.

## Recommendation for the meeting

- The meeting is invited to note the proposed option.

--------------------

Figure 1.  UML model of the proposed application schema to aggregate AvXML reports

Appendix I

Sample instance:

<?xml version="1.0" encoding="UTF-8"?>

<bulletin:Bulletin gml:id="Bulletin-00000001"

xmlns:bulletin="http://wmo.int/bulletin"

xmlns:gml="http://www.opengis.net/gml/3.2"

xmlns:iwxxm="http://icao.int/iwxxm/1.0"

xmlns:xlink="http://www.w3.org/1999/xlink"

xmlns:om="http://www.opengis.net/om/2.0"

xmlns:metce="http://def.wmo.int/metce/2013"

xmlns:sams="http://www.opengis.net/samplingSpatial/2.0"

xmlns:sf="http://www.opengis.net/sampling/2.0"

xmlns:saf="http://icao.int/saf/1.0"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://wmo.int/bulletin http://127.0.0.1:8080/fullmoon-required/wmo/bulletin/bulletin.xsd">

<bulletin:header>

<bulletin:MessageHeader>

<bulletin:messageDateTime>2013-10-03T06:13:34.266Z</bulletin:messageDateTime>

</bulletin:MessageHeader>

</bulletin:header>

<bulletin:metar>

<iwxxm:METAR gml:id="metar-YUDO-20120822163000Z" status="NORMAL" automatedStation="false">

<iwxxm:observation>

<om:OM_Observation gml:id="obs-03839-20120824T12Z">

<om:type xlink:href="http://codes.wmo.int/49-2/observation-type/IWXXM/1.0/MeteorologicalAerodromeObservation" xlink:title="Aerodrome Observation"/>

<!-- time at which the observation actually occured -->

<om:phenomenonTime>

<gml:TimeInstant gml:id="ti-201208221630Z">

<gml:timePosition>2012-08-22T16:30:00Z</gml:timePosition>

</gml:TimeInstant>

</om:phenomenonTime>

<!-- time at which the results of the observation were made available (10-minutes later) -->

<om:resultTime>

<gml:TimeInstant gml:id="ti-201208221640Z">

<gml:timePosition>2012-08-22T16:40:00Z</gml:timePosition>

</gml:TimeInstant>

</om:resultTime>

<om:procedure>

<metce:Process gml:id="p-49-2-metar">

<gml:description>WMO No. 49 Volume 2 Meteorological Service for International Air Navigation APPENDIX 3 TECHNICAL SPECIFICATIONS RELATED TO METEOROLOGICAL OBSERVATIONS AND REPORTS</gml:description>

</metce:Process>

</om:procedure>

<om:observedProperty xlink:href="http://codes.wmo.int/49-2/observable-property/MeteorologicalAerodromeObservation" xlink:title="Observed properties for METAR and SPECI (Meteorological Aerodrome Reports)"/>

<om:featureOfInterest>

<!-- featureOfInterest type and shape must refer to a point -->

<sams:SF_SpatialSamplingFeature gml:id="sampling-point-03839">

<sf:type xlink:href="http://www.opengis.net/def/samplingFeatureType/OGC-OM/2.0/SF_SamplingPoint" xlink:title="SF_SamplingPoint"/>

<sf:sampledFeature>

<!-- The aerodrome at which this observation took place -->

<saf:Aerodrome gml:id="uuid.dd062d88-3e64-4a5d-bebd-89476db9ebea">

<gml:identifier codeSpace="urn:uuid:">dd062d88-3e64-4a5d-bebd-89476db9ebea</gml:identifier>

<saf:designator>YUDO</saf:designator>

<saf:name>DONLON/INTERNATIONAL</saf:name>

<saf:locationIndicatorICAO>YUDO</saf:locationIndicatorICAO>

<saf:ARP>

<gml:Point gml:id="pt52284-32035" srsName="http://www.opengis.net/def/crs/EPSG/0/4326">

<gml:pos>12.34 -12.34</gml:pos>

</gml:Point>

</saf:ARP>

</saf:Aerodrome>

</sf:sampledFeature>

<sams:shape>

<!-- This is where the observation took place, assumed to be representative of the entire aerodrome -->

<gml:Point gml:id="point-5225-3201" srsDimension="2" srsName="http://www.opengis.net/def/crs/EPSG/0/4326">

<gml:pos>12.34 -12.34</gml:pos>

</gml:Point>

</sams:shape>

</sams:SF_SpatialSamplingFeature>

</om:featureOfInterest>

<!-- The result of the observation -->

<om:result>

<iwxxm:MeteorologicalAerodromeObservationRecord gml:id="or1" cloudAndVisibilityOK="false">

<iwxxm:airTemperature uom="Cel">17.0</iwxxm:airTemperature>

<iwxxm:dewpointTemperature uom="Cel">16.0</iwxxm:dewpointTemperature>

<iwxxm:qnh uom="hPa">1018</iwxxm:qnh>

<iwxxm:surfaceWind>

<iwxxm:AerodromeSurfaceWind variableDirection="false">

<iwxxm:meanWindDirection uom="deg">240</iwxxm:meanWindDirection>

<iwxxm:meanWindSpeed uom="m/s">4.0</iwxxm:meanWindSpeed>

</iwxxm:AerodromeSurfaceWind>

</iwxxm:surfaceWind>

<iwxxm:visibility>

<iwxxm:AerodromeHorizontalVisibility>

<iwxxm:prevailingVisibility uom="m">600</iwxxm:prevailingVisibility>

</iwxxm:AerodromeHorizontalVisibility>

</iwxxm:visibility>

<iwxxm:rvr>

<iwxxm:AerodromeRunwayVisualRange pastTendency="UPWARD">

<iwxxm:runway>

<saf:RunwayDirection gml:id="uuid.b1947d80-b7f7-11e2-9e96-0800200c9a66">

<gml:identifier codeSpace="urn:uuid:">b1947d80-b7f7-11e2-9e96-0800200c9a66</gml:identifier>

<saf:designator>12</saf:designator>

<saf:trueBearing uom="deg">118.23</saf:trueBearing>

<saf:elevationTDZ uom="m">20.5</saf:elevationTDZ>

<saf:usedRunway>

<saf:Runway gml:id="uuid.2f864fc0-b7f8-11e2-9e96-0800200c9a66">

<gml:identifier codeSpace="urn:uuid:">2f864fc0-b7f8-11e2-9e96-0800200c9a66</gml:identifier>

<saf:designator>12/30</saf:designator>

<saf:associatedAirportHeliport xlink:href="#uuid.dd062d88-3e64-4a5d-bebd-89476db9ebea"/>

</saf:Runway>

</saf:usedRunway>

</saf:RunwayDirection>

</iwxxm:runway>

<iwxxm:meanRVR uom="m">1000</iwxxm:meanRVR>

</iwxxm:AerodromeRunwayVisualRange>

</iwxxm:rvr>

<iwxxm:presentWeather xlink:href="http://codes.wmo.int/306/4678/DZ" xlink:title="Moderate Drizzle"/>

<iwxxm:presentWeather xlink:href="http://codes.wmo.int/306/4678/FG" xlink:title="Fog"/>

<iwxxm:cloud>

<iwxxm:AerodromeObservedClouds>

<iwxxm:layer>

<iwxxm:CloudLayer>

<iwxxm:amount xlink:href="http://codes.wmo.int/bufr4/codeflag/0-20-008/2" xlink:title="Scattered"/>

<iwxxm:base uom="ft">1000</iwxxm:base>

</iwxxm:CloudLayer>

</iwxxm:layer>

<iwxxm:layer>

<iwxxm:CloudLayer>

<iwxxm:amount xlink:href="http://codes.wmo.int/bufr4/codeflag/0-20-008/4" xlink:title="Overcast"/>

<iwxxm:base uom="ft">2000</iwxxm:base>

</iwxxm:CloudLayer>

</iwxxm:layer>

</iwxxm:AerodromeObservedClouds>

</iwxxm:cloud>

</iwxxm:MeteorologicalAerodromeObservationRecord>

</om:result>

</om:OM_Observation>

</iwxxm:observation>

<iwxxm:trendForecast>

<om:OM_Observation gml:id="trend-fcst-1">

<om:type xlink:href="http://codes.wmo.int/49-2/observation-type/IWXXM/1.0/MeteorologicalAerodromeTrendForecast" xlink:title="Aerodrome Trend Forecast"/>

<!-- time at which the forecast conditions actually occur -->

<om:phenomenonTime>

<gml:TimePeriod gml:id="tp-201208221630Z-201208221700Z">

<gml:beginPosition>2012-08-22T16:30:00Z</gml:beginPosition>

<gml:endPosition>2012-08-22T17:00:00Z</gml:endPosition>

</gml:TimePeriod>

</om:phenomenonTime>

<!-- time at which the results of the observation were made available -->

<om:resultTime xlink:href="#ti-201208221640Z"/>

<om:procedure xlink:href="#p-49-2-metar" xlink:title="WMO 49-2 METAR procedure"/>

<om:observedProperty xlink:href="http://codes.wmo.int/49-2/observable-property/MeteorologicalAerodromeTrendForecast" xlink:title="METAR trend forecast properties"/>

<om:featureOfInterest xlink:href="#sampling-point-03839"/>

<om:result>

<iwxxm:MeteorologicalAerodromeTrendForecastRecord gml:id="trend-fcst-record-03839-201208221630Z-201208221700Z" changeIndicator="BECOMING" cloudAndVisibilityOK="false">

<iwxxm:prevailingVisibility uom="m">800</iwxxm:prevailingVisibility>

<iwxxm:forecastWeather xlink:href="http://codes.wmo.int/306/4678/FG" xlink:title="Fog"/>

</iwxxm:MeteorologicalAerodromeTrendForecastRecord>

</om:result>

</om:OM_Observation>

</iwxxm:trendForecast>

<iwxxm:trendForecast>

<om:OM_Observation gml:id="trend-fcst-2">

<om:type xlink:href="http://codes.wmo.int/49-2/observation-type/IWXXM/1.0/MeteorologicalAerodromeTrendForecast" xlink:title="Aerodrome Trend Forecast"/>

<!-- time at which the forecast conditions actually occur -->

<om:phenomenonTime>

<gml:TimePeriod gml:id="tp-201208221800Z-201208221900Z">

<gml:beginPosition>2012-08-22T18:00:00Z</gml:beginPosition>

<gml:endPosition>2012-08-22T19:00:00Z</gml:endPosition>

</gml:TimePeriod>

</om:phenomenonTime>

<!-- time at which the results of the observation were made available -->

<om:resultTime xlink:href="#ti-201208221640Z"/>

<om:procedure xlink:href="#p-49-2-metar" xlink:title="WMO 49-2 METAR procedure"/>

<om:observedProperty xlink:href="http://codes.wmo.int/49-2/observable-property/MeteorologicalAerodromeTrendForecast" xlink:title="METAR trend forecast properties"/>

<om:featureOfInterest xlink:href="#sampling-point-03839"/>

<om:result>

<iwxxm:MeteorologicalAerodromeTrendForecastRecord gml:id="trend-fcst-record-03839-201208221800Z-201208221900Z" changeIndicator="BECOMING" cloudAndVisibilityOK="false">

<iwxxm:prevailingVisibility uom="km">10</iwxxm:prevailingVisibility>

<iwxxm:prevailingVisibilityOperator>ABOVE</iwxxm:prevailingVisibilityOperator>

<iwxxm:forecastWeather nilReason="http://codes.wmo.int/common/nil/nothingOfOperationalSignificance"/>

</iwxxm:MeteorologicalAerodromeTrendForecastRecord>

</om:result>

</om:OM_Observation>

</iwxxm:trendForecast>

</iwxxm:METAR>

</bulletin:metar>

</bulletin:Bulletin>